## Slide 1: Running SU2
SU2 Release Version 2.0 Workshop
Stanford University
Tuesday, January 15th, 2013
Sean Copeland & Tom Taylor
Department of Aeronautics & Astronautics
Stanford University

## Slide 2: Outline
SU2 environment variable
What do I need to run a simulation?
Test case definition
Interactive session
Questions?

## Slide 3: SU2 Environment Variables
Did you set your SU2 environment variables during the installation procedure?
i.e., in .bashrc:
# Set the SU2 source code home directory
export SU2_HOME=/Users/tomtaylor/SU2
# Identify directory where SU2 executables and python scripts are stored
Export SU2_RUN=/Users/tomtaylor/SU2Py
# Add SU2_RUN to the $PATH
Export PATH=$PATH:$SU2_RUN

## Slide 4: Running Simulations with SU2
What do I need to run simulations with SU2?
  Configuration file (.cfg)
  Mesh file (.su2 or .cgns)
This session will use:
  inv_NACA0012.cfg
  Mesh_NACA0012_inv.su2
These are found in
  > User Guide > Quick Start Tutorial
  /SU2/TestCases/inv_NACA0012/

## Slide 5: Test Case NACA 0012 Airfoil
Transonic, Euler flow
Mach No. = 0.8
Pressure = 101,325 Nm-2
Temperature = 273.15K
Angle of attack = 1.25o

## Slide 6: Flow Solution
Config options:
Most parameters have default values
Order of config options is not important
PHYSICAL_PROBLEM= EULER
%
MATH_PROBLEM= DIRECT
%
MACH_NUMBER= 0.8
%
AoA= 1.25
%
FREESTREAM_PRESSURE= 101325.0
%
FREESTREAM_TEMPERATURE= 273.15
%
MESH_FILENAME= mesh_NACA0012_inv.su2

## Slide 7: Restart
Simulations can be restarted from partially converged results
Config options:
RESTART_SOL= NO
%
EXT_ITER= 50
RESTART_SOL= YES
%
SOLUTION_FLOW_FILENAME= solution_flow.dat

## Slide 8: Solver Parameters
Among the many options in the config file, various parameters exist to modify the solution method
Config options:
RESTART_SOL= NO
%
CFL_NUMBER= 4.0
%
CFL_RAMP= ( 1.1, 10, 10.0 )
%
CONV_NUM_METHOD_FLOW= ROE-2ND_ORDER

## Slide 9: Adjoint Solution
Sensitivity of a functional to changes in the flow
  e.g., How does changing the airfoil shape affect lift?
Additional required file:
  Converged flow solution
Config options:
MATH_PROBLEM= ADJOINT
%
RESTART_SOL= NO
%
ADJOINT_TYPE= CONTINUOUS
%
ADJ_OBJFUNC= DRAG
%
SOLUTION_FLOW_FILENAME= solution_flow.dat

## Slide 10: Example: Separated Flow Over Cylinder

## Slide 11: Example: Tip Vortices From Rotor

## Slide 12: Additional Resources
Online documentation
  http://su2.stanford.edu
Online tutorials
  > User Guide > User’s Guide > User’s Tutorials
TestCases directory
  /SU2/TestCases/
CFD Online forum
  http://www.cfd-online.com/Forums/su2/