## Slide 1: SU2 Design Exploration NACA 0012
SU2 Release Version 2.0 Workshop
Stanford University
Tuesday, January 15th, 2013
Trent Lukaczyk
Department of Aeronautics & Astronautics
Stanford University

## Slide 2: Indirect Design Approaches
2
Example: Response Surface Modeling
Two Hicks-Henne Bump Functions
10x10 grid of simulations

## Slide 3: Indirect Design Approaches
3
Example: Response Surface Modeling
Two Hicks-Henne Bump Functions
10x10 grid of simulations

## Slide 4: Task-Based Design Exploration
4
Task Deformation
Project
Root folder of data Baseline config and mesh
Task Direct Solution
Task Drag Adjoint
Task Lift Adjoint
Config Change
Job 0
Contains analysis tasks Output meshes, restarts
Job 1
Config Change
Job 2
Config Change
* Only design variables for now

## Slide 5: NACA0012 Test Case
5
NACA 0012 Test Case
One Hicks-Henne Bump Function
11 Evaluations in X ϵ [-0.02 , 0.02]
Notes: Describe the test case
Plot with matplotlib
Liberate to matlab with scipy
Find the files located in the testcases directory
Copy to a new location

## Slide 6: config_NACA0012.cfg
6
% ------------------------- EVALUATE PROJECT DEFINITION ------------------------%
% List of tasks to complete
TASKS= DEFORM, DIRECT, CONT_ADJOINT
% Number of partitions (0 for Serial)
NUMBER_PART= 2
% List of design variables (Design variables are separated by semicolons)
% - HICKS_HENNE: ( 1, Scale | Mark. List | Lower(0)/Upper(1) side, x_Loc )
DEFINITION_DV= ( 1, 1.0 | airfoil | 0, 0.05 ); ( 1, 1.0 | airfoil | 0, 0.10 ); (...)
% Gradients to calculate
GRADIENTS= LIFT, DRAG, MOMENT_Z
% Console output (VERBOSE, CONCISE, QUIET)
CONSOLE= CONCISE
Notes: Open config_NACA0012.cfg

## Slide 7: config_NACA0012.cfg
7
% ------------------------- EVALUATE PROJECT DEFINITION ------------------------%
% List of tasks to complete
TASKS= DEFORM, DIRECT, CONT_ADJOINT
% Number of partitions (0 for Serial)
NUMBER_PART= 2
% List of design variables (Design variables are separated by semicolons)
% - HICKS_HENNE: ( 1, Scale | Mark. List | Lower(0)/Upper(1) side, x_Loc )
DEFINITION_DV= ( 1, 1.0 | airfoil | 0, 0.05 ); ( 1, 1.0 | airfoil | 0, 0.10 ); (...)
% Gradients to calculate
GRADIENTS= LIFT, DRAG, MOMENT_Z
% Console output (VERBOSE, CONCISE, QUIET)
CONSOLE= CONCISE

## Slide 8: config_NACA0012.cfg
8
% ------------------------- EVALUATE PROJECT DEFINITION ------------------------%
% List of tasks to complete
TASKS= DEFORM, DIRECT, CONT_ADJOINT
% Number of partitions (0 for Serial)
NUMBER_PART= 2
% List of design variables (Design variables are separated by semicolons)
% - HICKS_HENNE: ( 1, Scale | Mark. List | Lower(0)/Upper(1) side, x_Loc )
DEFINITION_DV= ( 1, 1.0 | airfoil | 0, 0.05 ); ( 1, 1.0 | airfoil | 0, 0.10 ); (...)
% Gradients to calculate
GRADIENTS= LIFT, DRAG, MOMENT_Z
% Console output (VERBOSE, CONCISE, QUIET)
CONSOLE= CONCISE

## Slide 9: config_NACA0012.cfg
9
% ------------------------- EVALUATE PROJECT DEFINITION ------------------------%
% List of tasks to complete
TASKS= DEFORM, DIRECT, CONT_ADJOINT
% Number of partitions (0 for Serial)
NUMBER_PART= 2
% List of design variables (Design variables are separated by semicolons)
% - HICKS_HENNE: ( 1, Scale | Mark. List | Lower(0)/Upper(1) side, x_Loc )
DEFINITION_DV= ( 1, 1.0 | airfoil | 0, 0.05 ); ( 1, 1.0 | airfoil | 0, 0.10 ); (...)
% Gradients to calculate
GRADIENTS= LIFT, DRAG, MOMENT_Z
% Console output (VERBOSE, CONCISE, QUIET)
CONSOLE= CONCISE

## Slide 10: config_NACA0012.cfg
10
% ------------------------- EVALUATE PROJECT DEFINITION ------------------------%
% List of tasks to complete
TASKS= DEFORM, DIRECT, CONT_ADJOINT
% Number of partitions (0 for Serial)
NUMBER_PART= 2
% List of design variables (Design variables are separated by semicolons)
% - HICKS_HENNE: ( 1, Scale | Mark. List | Lower(0)/Upper(1) side, x_Loc )
DEFINITION_DV= ( 1, 1.0 | airfoil | 0, 0.05 ); ( 1, 1.0 | airfoil | 0, 0.10 ); (...)
% Gradients to calculate
GRADIENTS= LIFT, DRAG, MOMENT_Z
% Console output (VERBOSE, CONCISE, QUIET)
CONSOLE= CONCISE

## Slide 11: config_NACA0012.cfg
11
% ------------------------- EVALUATE PROJECT DEFINITION ------------------------%
% List of tasks to complete
TASKS= DEFORM, DIRECT, CONT_ADJOINT
% Number of partitions (0 for Serial)
NUMBER_PART= 2
% List of design variables (Design variables are separated by semicolons)
% - HICKS_HENNE: ( 1, Scale | Mark. List | Lower(0)/Upper(1) side, x_Loc )
DEFINITION_DV= ( 1, 1.0 | airfoil | 0, 0.05 ); ( 1, 1.0 | airfoil | 0, 0.10 ); (...)
% Gradients to calculate
GRADIENTS= LIFT, DRAG, MOMENT_Z
% Console output (VERBOSE, CONCISE, QUIET)
CONSOLE= CONCISE

## Slide 12: run_project.py
12
# Setup
(…)
# design variable values
DV_vals = numpy.linspace(-0.02,0.02, 11 )
# setup config changes
config_delta = []
for X in DV_vals:
DV_X = numpy.zeros(n_DV)
DV_X[i_DV] = X
config_delta.append( {'VARIABLES':DV_X} )
# initialize project
The_Project = Project( config_name = config_filename ,
design_name = design_filename )

## Slide 13: run_project.py
13
# Setup
(…)
# design variable values
DV_vals = numpy.linspace(-0.02,0.02, 11 )
# setup config changes
config_delta = []
for X in DV_vals:
DV_X = numpy.zeros(n_DV)
DV_X[i_DV] = X
config_delta.append( {'VARIABLES':DV_X} )
# initialize project
The_Project = Project( config_name = config_filename ,
design_name = design_filename )

## Slide 14: run_project.py
14
# Setup
(…)
# design variable values
DV_vals = numpy.linspace(-0.02,0.02, 11 )
# setup config changes
config_delta = []
for X in DV_vals:
DV_X = numpy.zeros(n_DV)
DV_X[i_DV] = X
config_delta.append( {'VARIABLES':DV_X} )
# initialize project
The_Project = Project( config_name = config_filename ,
design_name = design_filename )
List of Variable Settings:
[ {‘VARIABLES’:-0.020} ,
{‘VARIABLES’:-0.018} ,
…
{‘VARIABLES’:+0.020} ]

## Slide 15: run_project.py
15
# Setup
(…)
# design variable values
DV_vals = numpy.linspace(-0.02,0.02, 11 )
# setup config changes
config_delta = []
for X in DV_vals:
DV_X = numpy.zeros(n_DV)
DV_X[i_DV] = X
config_delta.append( {'VARIABLES':DV_X} )
# initialize project
The_Project = Project( config_name = config_filename ,
design_name = design_filename )

## Slide 16: run_project.py
16
# Run Project
# evaluate project
design_new,_,_ = The_Project.evaluate(config_delta)
# save project
libSU2.save_data(project_filename,The_Project)
# save data
# already done by The_Project.evaluate()