## Slide 1: Running SU2
Pointwise® and SU2 Joint Workshop
Sept 29th-30th, 2014
Heather Kline, Andrew Wendorff
Aeronautics & Astronautics Department (Stanford University)

## Slide 2
What do I need to run a simulation?
Test case definition
Interactive session
Questions?

## Slide 3: Running Simulations with SU2
What do I need to run simulations with SU2?
  Configuration file (.cfg)
  Mesh file (.su2 or .cgns)
This session will use:
  lam_NACA0012.cfg
  Mesh_NACA0012_lam_omesh.su2
These are found in
  su2.stanford.edu > Training
  github.com/su2code/TestCases/

## Slide 4: Test Case NACA 0012 Airfoil
Transonic, Euler flow
Mach No. = 0.5
Pressure = 101,325 Nm-2
Temperature = 288.15K
Angle of attack = 1.0o
Reynolds number = 1,000

## Slide 5: Flow Solution
Config options:
Most parameters have default values
The order of config options is not important
PHYSICAL_PROBLEM= NAVIER_STOKES
%
MATH_PROBLEM= DIRECT
%
MACH_NUMBER= 0.5
%
AoA= 1.00
%
REYNOLDS_NUMBER=1000.0
%
FREESTREAM_TEMPERATURE= 288.15
%
MESH_FILENAME= mesh_NACA0012_lam_omesh.su2

## Slide 6: Restart
Simulations can be restarted from partially converged results
Config options:
RESTART_SOL= NO
%
EXT_ITER= 999999
RESTART_SOL= YES
%
SOLUTION_FLOW_FILENAME= solution_flow.dat

## Slide 7: Solver Parameters
Among the many options in the config file, various parameters exist to modify the solution method
Config options:
RESTART_SOL= NO
%
CFL_NUMBER= 4.0
%
CFL_RAMP= ( 1.1, 10, 10.0 )
%
CONV_NUM_METHOD_FLOW= ROE
%
SPATIAL_ORDER_FLOW= 2ND_ORDER

## Slide 8: Interactive
Direct Solution
Notes: Budgeted time: 10 minutes

## Slide 9: Adjoint Solution
Sensitivity of a functional to changes in the flow
  e.g., How does changing the airfoil shape affect lift?
Additional required file:
  Converged flow solution
Config options:
MATH_PROBLEM= ADJOINT
%
RESTART_SOL= NO
%
ADJOINT_TYPE= CONTINUOUS
%
ADJ_OBJFUNC= DRAG
%
SOLUTION_FLOW_FILENAME= solution_flow.dat
Notes: Change restart_flow.dat to solution_flow.dat
Copy config file, change settings

## Slide 10: Interactive
Adjoint Solution
Notes: Start : won’t finish in time, go to example results

## Slide 11: Additional Resources
Online documentation
  http://su2.stanford.edu
Online tutorials
  su2.stanford.edu > Training
  also accessible via su2.stanford.edu > Guides > User’s Tutorials
TestCases directory
  github.com/su2code/TestCases/
CFD Online forum
  http://www.cfd-online.com/Forums/su2/

## Slide 12: Questions?